## Slide 1: trace_simexp: a Python Package
TRACE Launcher
The trace_simexp package is a python package that responsible solely to launch and manage statistical simulation of TRACE. Its operations are mainly in the shell level
Design Matrix
Base TRACE
List of Parameters
Inputs
Prepo
Perturb the TRACE parameters listed in the list of parameters file according to the values specified in design matrix
Generate directory structures that contains spawned trace input decks
Execute
Submit and manage TRACE jobs in parallel (in sequential batches)
Convert XTV to DMX to save space
Do directory cleanup to further reduce space requirements
Post-process
Perturb the TRACE parameters listed in the list of parameters file according to the values specified in design matrix
Generate directory structures that contains spawned trace input decks
List of Graphic Variables
CSV
To enforce reproducibility, the simulation campaign parameters (the three inputs file, the number of processors, the location of scratch, the samples to be executed, etc.) have to be specified as command line arguments (which should be recorded). Log files from each step will be produced.
Ready to be post- processed further by GSA methodologies
Can be prepared by a generic GSA toolbox
(e.g., SIMLAB)

## Slide 2
TRACE Launcher
Prepro
Perturb the TRACE parameters listed in the list of parameters file according to the values specified in design matrix
Generate directory structures that contains spawned trace input decks
Execute
Submit and manage TRACE jobs in parallel (in sequential batches)
Convert XTV to DMX to save drive space
Do directory cleanup to further reduce the space requirements
Post-process
Postprocess each xtv files and extract the variables listed in the list of graphic variables file into separate csv files.
List of Graphic Variables
CSV
Ready to be post- processed further sensitivity analysis tool
Base TRACE
List of Parameters
Design Matrix
TRACE Executable
Aptplot Executable
Inputs & Aux files
Driver Scripts
Outputs
prepro info file
exec info file
postpro info file
Notes: Generic flowchart of trace-simexp